## Slide 1
GROUP 28
PRS PRACTICE MODULE · PROJECT PROPOSAL
Indoor Dog Behavior &
Human–Dog Interaction
Recognition via dual-species RTMPose skeletons + ST-GCN temporal modeling
ZHAO JIAYI · SUN WENJING · GROUP 28

## Slide 2: Pet Cameras See, but Don't Understand
01 · BACKGROUND
WHY THIS PROJECT
MARKET · 2024
Pet cameras go mainstream
Owners treat dogs as family and want to know they are safe and well while away.
$198M
Global market size, 2024
GROWTH · 2024–2030
Demand keeps growing
Expected to reach ~$454M by 2030, driven by owners treating pets as family.
12.6%
Compound annual growth rate
GAP
Today's products only "see"
Detect, track, push alerts. Did the dog eat? Did anyone play with it? Owners still scrub the footage.
Understand
The step this project adds
Source: Grand View Research, Pet Monitoring Camera Market Report

## Slide 3: Make the Camera Understand the Dog
02 · OBJECTIVES
GOAL · A WORKING VIDEO-ANALYSIS PROTOTYPE
Upload an indoor video → get dog behavior, interaction type, confidence and a timeline.
TASK A
Dog Behavior Recognition
Dog only: infer what it is doing from how its skeleton moves over time.
Input: dog skeleton sequence T × 17 × 3
Model: ST-GCN (LSTM baseline)
8 classes: stand · walk · run · sit · lie/sleep · eat/drink · play · other
TASK B
Human–Dog Interaction
Human and dog together: motion + human–dog relation + sound.
Input: human + dog skeletons + relation features (optional audio)
Model: dual-stream ST-GCN, late fusion
4 classes: none · feeding · petting · playing together

## Slide 4: System Architecture
03 · SYSTEM & DATA
SYSTEM OVERVIEW
Offline: dog pose AP-10K → APT-36K dogs → indoor data; human pose COCO-17
Online in 6 steps: video → detect/track → pose → skeleton graph → recognition → output
Tracking: RTMDet / YOLO + ByteTrack / BoT-SORT
Dual-species skeletons are the shared representation: pose estimation sees the joints, ST-GCN understands the motion.
INFERENCE
6
Video in, JSON + timeline out
TASKS
2
Task A behavior · Task B interaction
METRICS
4
AP / PCK · Acc / Macro-F1

## Slide 5: Where the Data Comes From
03 · SYSTEM & DATA
DATA PREPARATION
① APT-36K: official split, dog samples only, no re-labeling
② Online videos: Group ID per dog + full video, split first, then sample frames and clips
Split first, sample later: one dog or video never spans train and test
AP-10K is RTMPose's pretraining set, so we don't train on it again; public dog pose data comes from APT-36K.
SOURCES
2
APT-36K dogs · indoor videos
FRAME LABELS
300–800
indoor images: dog box + 17 keypoints
OUTPUTS
3
Keypoints · clip labels · derived features

## Slide 6: Training Dog Pose
03 · SYSTEM & DATA
DOG POSE ADAPTATION
P0: official AP-10K RTMPose-M, tested as-is (baseline)
P1: fine-tune on the APT-36K dog subset
P2: keep fine-tuning on indoor data with a small learning rate
One shared test set. If P1 beats P0, dog specialization helps; if P2 beats P1, indoor adaptation helps.
VERSIONS
3
P0 → P1 → P2, stage by stage
TEST SET
1
One held-out test set for all three
POSE METRICS
4
COCO AP · AP@0.5 · AP@0.75 · PCK

## Slide 7: Dual-Species Skeleton Extraction
04 · MODEL DESIGN
ONLINE STEP 03 · POSE
Human and dog branches share one design: affine crop → CSPNeXt-M → RTMCCHead → SimCC
Only input size differs (human 256×192, dog 256×256); no shared weights
Aligned across frames by track ID, then masked, interpolated and smoothed
RTMCCHead = 7×7 conv + FC + GAU; SimCC turns coordinate regression into classification.
BACKBONE
768
CSPNeXt-M output channels
KEYPOINTS
17
Human COCO · dog AP-10K
OUTPUT
2×T×17×3
2 streams · x, y, confidence

## Slide 8: How Graph Convolution Works
04 · MODEL DESIGN
ST-GCN PRINCIPLE
Example: human right elbow and dog left elbow with their 1-hop neighbors (D = 1)
Uni-labeling: 1 group; distance: root / 1-hop, 2 groups
Spatial configuration: root, centripetal, centrifugal by distance to the center of gravity, 3 groups
Both networks use spatial configuration partitioning: one adjacency matrix per group, A₀, A₁, A₂.
STRATEGIES
3
Uni-label · distance · spatial
NEIGHBORHOOD
D = 1
Root node and 1-hop neighbors
ADJACENCY
A₀ A₁ A₂
Spatial config., shared by Task A / B

## Slide 9: Task A Dog Behavior
04 · MODEL DESIGN
ONLINE STEP 05 · TASK A
Follows the original ST-GCN (Yan et al., AAAI 2018)
9 residual units in 3 stages: channels 64 → 128 → 256, time T → T/2 → T/4
Global average pooling → Linear + Softmax; baseline: LSTM
Each unit: spatial graph conv (A₀–A₂), then 9×1 temporal conv, then residual add.
RESIDUAL UNITS
9
3 stages × 3 units
FEATURE
256-D
After global average pooling
CLASSES
6
Stand · sit · lie · eat · play · other

## Slide 10: Task B Interaction
04 · MODEL DESIGN
ONLINE STEP 05 · TASK B
Human and dog skeletons each go through an ST-GCN → f_h and f_d
Plus relation features f_r (distance, velocity, orientation) and optional audio (YAMNet / MERT)
Concat + MLP at the end: late fusion
Late fusion keeps audio optional: with no or poor sound, the skeletons alone still give a prediction.
STREAMS
2
Human + dog, one ST-GCN each
RELATION
3
Distance · velocity · orientation
CLASSES
4
None · feeding · petting · play

## Slide 11: How We Prove Each Step Works
05 · EVALUATION
EVALUATION PLAN
01 / POSE
Pose
COCO AP · AP@0.5 · AP@0.75 · PCK
P0 / P1 / P2 on the same test set, reported for head, forelimbs and hindlimbs.
02 / TASK A
Dog Behavior
Accuracy · Macro-F1 · confusion matrix
LSTM vs ST-GCN; ablate confidence, missing-joint handling, skeleton augmentation.
03 / TASK B
Interaction
Same metrics + ablations
Single vs dual stream
± relation features
± audio
04 / SPLIT
Robustness
Unseen dogs and scenes
Split by dog + full video
Occlusion, missing joints
Multi-subject, no audio
RULE
Val set for model selection only; test set used once at the end, the same one for every comparison.

## Slide 12
12 / 12
THANK YOU
Q&A
GROUP 28 · ZHAO JIAYI · SUN WENJING
TAKEAWAYS
01
Skeletons link everything
Pose estimation sees joints; ST-GCN understands motion over time.
02
Every step is testable
P0 → P1 → P2 and ablations answer "does it help?" one by one.
03
Leak-free data split
Grouped by dog and full video: we test on unseen dogs and scenes.